## Slide 1: Care and Maintenance of Portable Meters
2017 Meter Technician Training School
Steven Sievert
Manager, Quality Certification Services Inc.
Technical Director, National DHIA
Chair, ICAR Subcommittee for Recording and Sampling Devices

## Slide 2: Topics to Cover…
      Maintenance of Approved Meters
      Storage and Transport of Meters
      Proper Sampling and Reading

## Slide 3: Maintenance of Approved Meters

## Slide 4: Tru-Test Pull-Out
Most popular meter in Northeast and Midwest
Easy to maintain
Standard Bore (old) or Wide Bore (new) models
Labor intensive operation
Low cost of ownership

## Slide 5: Tru-Test Pull-Out - Maintenance
Replace VSO at least once per year
Replace gasket on cap yearly
Replace the flask plug yearly or when breakdown of rubber is noticeable
1
2
4

## Slide 6: Tru-Test Pull-Out - Maintenance
Inspect nozzle, replace only when meter does not calibrate
  Remove with fingers – not pliers, etc.
  Do not reuse nozzles

## Slide 7: Tru-Test Pull-Out - Maintenance
Flask plug improvements have been made
Thicker base
Tolerances changed to fit & seal better to flask
Look for 3 dot pips under the base for the improved flask plugs

## Slide 8: Tru-Test Pull-Out - Maintenance
New laser-etched flasks – do not use flask tapes on flasks for WB meters

## Slide 9: Tru-Test Ezi-Test
Most popular meter in the world
Milk, Wash/Mix and Sample positions
Standard Bore (old) or Wide Bore (new) models
Self-contained (closed system)

## Slide 10: Tru-Test Ezi-Test - Maintenance
Replace gasket on cap yearly
Inspect nozzle, replace only when meter does not calibrate
  Remove with fingers – not pliers, etc.
  Do not reuse nozzles

## Slide 11: Tru-Test Ezi-Test – Annual Service Kits

## Slide 12: Tru-Test Ezi-Test – Flask Seal
Replace flask seal

## Slide 13: Tru-Test Ezi-Test - Maintenance
Replace rocker and seal assembly
Check and replace air admission valve seal when necessary
  Do not over tighten screw

## Slide 14: Tru-Test Ezi-Test - Maintenance
Plastic T-Piece
  Easily broken
  $20+ repair cost
Store with valve in Milk Position

## Slide 15: Tru-Test Ezi-Test - Maintenance
Must replace entire valve
Dark charcoal in color
Should reduce broken wash baffle issue

## Slide 16: Tru-Test Ezi-Test - Grommets

## Slide 17: Tru-Test Auto-Sampler
Mixing and sampling with push of button
Labor-efficient
Standard Bore (old) or Wide Bore (new) models
High cost of ownership
  Multiple service kits
  Cap, sampler, valve and body damage

## Slide 18: Tru-Test Auto Sampler - Maintenance
Replace gasket on cap yearly
Inspect nozzle, replace only when meter does not calibrate
  Remove with fingers – not pliers, etc.
  Do not reuse nozzles

## Slide 19: Tru-Test Auto Sampler – Service Kits

## Slide 20: Tru-Test Auto Sampler – Maintenance

## Slide 21: Tru-Test Auto Sampler - Maintenance
Replace rocker and seal assembly
Replace push button and O-ring

## Slide 22: Tru-Test Auto Sampler – Flask Seal
Replace flask seal

## Slide 23: Tru-Test Auto Sampler - Maintenance
Must replace entire valve
Dark charcoal in color
Should reduce broken wash baffle issue

## Slide 24: Tru-Test Auto Sampler - Grommets

## Slide 25: Tru-Test Auto-Sampler – Sampler Dial
New Calibration Label
  Weight Levels
  Zones – Low/Med/High
New Ring
  Snap Fit
Dark Grey in Color

## Slide 26: Tru-Test Auto-Sampler – Sampler
Replace O-ring on Sampler

## Slide 28: Tru-Test Farmer and Econo-Valve
Only Standard Bore models
Over 30 years old
No parts available
Dated image of DHI
Still approved but should be removed from service?

## Slide 29: Foss Milko-Scope
Volumetric Meter
No longer manufactured but DeLaval owns patent
Reliable and accurate
Durable except for bracket
Larger vacuum drop
  Larger dome
  Small inlet (similar to SB)

## Slide 30: Waikato MK V
Same mode of operation as Ezi-Test
Annual Service Kit
Don’t forget to replace inlet hoses
Durable
Larger vacuum drop
  Larger dome
  More prevalent in large parlors

## Slide 31: Waikato SpeedSampler
Annual Service Kit
Sampler Service Kit
Don’t forget to replace inlet hoses
Check all hoses for cracks or leaks
Check bungs for wear and ensure lifter arm is properly positioned

## Slide 32: Unapproved DHI Meters – Mini-Test
Not ICAR Approved
Weighing and sampling accuracy does not meet tolerances
Farmer Use only
  SCC checks between test days
  Does not matter what test plan – cannot use for DHI

## Slide 33: Unapproved DHI Meters - TeSa
Never ICAR Approved
Weight principle – not volumetric principle
No parts available
National DHIA/QCS acceptance expired on December 31, 2010

## Slide 34: Unapproved DHI Meters - Bodmin
Never ICAR Approved
Significant sampling issues
  Milk fat variance as high as 52%
  SCC variance as high as 34%

## Slide 35: Unapproved DHI Meters - Flaco
Imitation Waikato meter manufactured in China
Not ICAR approved
Accuracy and parts quality questionable

## Slide 36: Meter Repair Tags
Space for Tester Name, Date & Problem
Quick ID of the problem
Reduces down time
Trace back and accountability

## Slide 37: Meter Storage and Transport

## Slide 38: Meter Storage
Plastic totes provide convenient storage
of up to 10 meters

## Slide 39: Meter Storage & Transportation
Totes are easily carried into milk barn for setup
Totes cost approximately $10-$12
One replacement meter costs approximately $400

## Slide 40: Meter Storage & Transportation
Truck bed cover keeps everything secure
Truck cover=$900
30 stolen meters=$10,500
Trailer transport for large herds

## Slide 41: Meter Storage & Transportation
PVC pipe racks
Holds 8 meters with Super Clamps
Plans in Meter Technician Manual

## Slide 42: Meter Storage & Transportation
PVC pipe racks
Holds 10 meters with Dovetail Brackets
Easy transport and minimal damage (if any)
Plans in Meter Technician Manual

## Slide 43: Meter Mask
Protects against meter body damage from teat cups and premature meter draining
Meter Mask= $20.00
Meter Body=$190.00

## Slide 44: Heavy Duty Meter Cleaning

## Slide 45: Proper Sampling and Reading

## Slide 46: Sample Mixing Research
Minnesota DHIA Trial
Used Tru-Test Pull-Out meters with 68# & 102# meters
Removed flasks during milking, mixing thirds before sampling
Simply poured milk without mixing

## Slide 47: 58# milk in 102# Tru-Test Pullout Meter poured without mixing

## Slide 48: 51# of milk in 68# Tru-Test Pullout Meter

## Slide 49: 65# milk in 102# Tru-Test Pullout Meter

## Slide 50: 37# of milk in 68# Tru-Test Meter

## Slide 51: Findings on Sample Mixing
Employ proper mixing of flask milk for every cow
  Pull-Out Flasks – minimum of 2x (4x recommended)
  Ezi-Test Meters – 10 seconds if flask is more than ½ full
  Ezi-Test Meters – 5 seconds if flask is less than ½ full
  Waikato Meters – 10 seconds
  May need to be twice as long in cold weather/cold parlors
Fill sample vials immediately and shake to disperse preservative
DHIA laboratories have protocols in place for sample handling and mixing before analysis

## Slide 52: Reading the Flask Volume
Read the BOTTOM of the meniscus
Foam does NOT count
Read between the lines
  1 lb marks – read to ½ lb
  ½ lb marks – read to ¼ lb
Consistent reading from start to finish
Replace worn flasks

## Slide 53
Does the milking cluster have an effect?
Reports of challenges with FloStar claws
Claw is designed to encourage milk pooling and empties in a ‘sump pump’ fashion
There is a not a steady milk flow to portable volumetric meters
DHI meters read about 3-5% lower than on-farm fill-and-dump meters (Perfection) on total milk yield.
Test Day/Milk Shipped Deviations < 96%

## Slide 54: Test Day/Milk Shipped Deviations < 96%
Older Standard Bore Tru-Test meters & Waikato meters accurately proportion milk at flow rates up to 24 lbs/minute
May be underestimating milk yield during peak flow rates – possibly 3-5% of total milk yield
Need to use the right equipment for the job
  Wide Bore (WB) meters accurately proportion milk at flow rates up to 32 lbs/minute
  How well do they wash/clean?

## Slide 55: Test Day/Milk Shipped Deviations > 110%
Use of Milkrite impulseAir, Lauren, or Conewango vented inflations
Changes the milk-air ratio in the cluster/milk line – exceeds the ISO standard for air flow of 30 liters per minute
Tru-Test meters (all ICAR certified meters) are tested and approved to operate within ISO tolerances for air flow
Tru-Test WB meters may read 6-10% high (usually around 7-8%)

## Slide 56: Testing for Potential Effect of Vented Inflations
The ICAR Recording and Sampling Devices SC (RSD-SC) met in February 2017
Similar concerns from Canada, UK, Denmark, Germany, Poland, France and Netherlands regarding vented inflations
Manufacturers slow to comment as these inflations are non OEM equipment
RSD-SC is planning a test of effect of vented inflations on milk meters
  5 classes of meters
  3 milk flow rates (3, 6, & 9 kg/minute)
  9 air admission rates (including 3 that exceed ISO specifications

## Slide 57: Some Final Thoughts on Meters
EQUIPMENT PERFORMANCE
FIELD TECHNICIAN PERFORMANCE
Start with clean, sanitized meters
Minimize hose length
  Reduce vacuum loss
  May have to have different hoses for different dairies
Clean the outside as well as the inside
  CIP is NOT enough!
  Protect meters – wax, etc.
Service and repair meters often
  Share what is going on!
  Replace VSO & gaskets
Read the meters properly without any influence from dairy owner
Use proper sampling and mixing techniques

## Slide 58: Your Challenge is…
You control your image…
  Professional appearance
  Properly operating equipment
  Proper technique
  Exceed the minimum requirements
  Communicate your needs with management
Resulting in…
  Accurate and consistent results
  Fewer concerns and/or complaints from dairymen
  Customer retention and satisfaction

## Slide 59: Quality Certification Services Inc.
A simple, yet vital mission….
Providing a reliable source of information to people interested in the U.S. dairy records industry.
Performance & Quality Standards
Compliance Auditing of Providers
Education, Training, & Development